## Slide 1
Parts arrangement

## Slide 2
Balls are fed one by one, with geared feeding mechanism.
Main drum rotates ¼ of a circle per ball.
Eject rail rotates to switch the path of exiting ball.
Existence of next ball is sensed by a vertical lever.
Mechanism (1)

## Slide 3
Main drum rotates ¼ circle (90 degrees) per ball.
Gear ratio is 1:4. Escapement wheel rotates 1 full turn per ball.
Escapement wheel has 40 teeth.
Period of the pendulum is 0.75 sec.
  30 seconds per ball.
  Theoretical pendulum length is 14cm.
Feed drum also rotates 1 full turn per a ball, of course.
Mechanism (2)

## Slide 4
I used 11mm steel ball. My design could be scaled for larger balls. I offer the other gear (different reduction ratio) for the larger cases which has strong force from heavy steel balls. I used 1.6mm stainless wire for shafts. It needs careful check of straightness.
I used small and cheap bell for bicycle. You can use generic base plate for your own casing / bell arrangement.

## Slide 5
All shafts should be prepared separately
  I used 1.6mm stainless wire
  Lengths are 2.0, 3.8, 3.3mm (top to down)
All holes are just guides for drilling
  For tight holes, use a bit thinner drill
    I used 1.5mm drill
    Shafts are hammered in
  For loose holes, I used 2mm drill
    Make sure it rotates smoothly
T
T
T
T
T
T
L
L
L
L
T
glued or weld
glued or weld
Main pendulum unit

## Slide 6
All shafts should be prepared separately
  I used 1.6mm stainless wire
  Lengths are 2.1 and 1.5mm (top to down)
All holes are just guides for drilling
  For tight holes, use a bit thinner drill
    I used 1.5mm drill
    Shafts are hammered in
  For loose holes, I used 2mm drill
    Make sure it rotates smoothly
T
T
L
L
T
glued or weld
Feed / eject unit
L
L
T
T
two units can be assembled separately.

## Slide 7
Drill all holes for shafts.
Not to be oblique, or parts interfere each other.
Make sure that all shafts are straight.
  Shafts should be hammered in at tight fit.
  Especially, feed axis should be tight.
Assembly (1)

## Slide 8
Make sure that all parts keep adequate gaps each other. In case of oblique drilling, rotating part touches the other easily.
Use washers to adjust the gaps. Numbers and positions of washers are not limited to the left figure.
If parts interfere each other, use more washers. Expand the base plate to the depth direction. Axis of escapement wheel is already a bit longer.
Assembly (2)
washer
washer

## Slide 9
Weight should be inserted to the weight.stl object. You can also use the steel ball for this machine as weight.
In case of jamming at eject step, bend the tongue of eject rail upward slightly. Use hair drier to soften the the material. Be careful not to overheating.
Assembly (3)

## Slide 10
Bend here
Make sure that gap at two dead points are same. To tune it, use the balance of weights, or bend the pendulum by heating it with hair drier. Do not overheat.
Most 3D printer can not reproduce the precise shape of escapement. Carve the edge of pallets with sharp knife.
Pendulum tuning